## Slide 1: Improving Movement Direction of a road user using Compass Bearing and Orientation
Project Work
By
Vineela Pulagura
Supervised by
Mr. Johann Götz
20-05-2022

## Slide 2: Outline
Introduction
Sensors
Application Specifications
Raw Measurements
Orientation Sensor
SOMDA
Orientation method
Fused Orientation
Comparison of Orientation sensor and Fused Orientation approach
Conclusion and Future Works

## Slide 3: Introduction
Around 6.64 billion as of March 2022 [1].
Characteristics
  Low cost
  Small size
  Portability
  Embedded with sensors
Applications
  Human activity recognition
  Indoor and outdoor navigation
  Augmented reality
  Pedestrian collision avoidance
Fig1. Smartphones around the world [1]

## Slide 4: Introduction
What is the need of movement direction detection?
  Applications like pedestrian collision avoidance
Existing approaches
  Global Position System (GPS) based heading estimation
    Battery problem
    Less accurate positioning
  Movement direction estimation using visual tracking and map information
    Requires the map of the location
  Smartphone Orientation and Movement Direction Alignment (SOMDA)

## Slide 5: Introduction
Misalignment of user frame with the device frame
Orientation sensor deprecation
Reference Coordinate System [3]
User Frame and Device Frame [2]

## Slide 6: Introduction
Goal
  Improve the movement direction detection using SOMDA
  Evaluation
  Compare with the existing approach

## Slide 7: Sensors
Sensor | Details
Accelerometer | Measures the linear acceleration in X, Y and Z axes in
Magnetometer | Measures the magnetic field in X, Y and Z axes in
Gyroscope | Measures the angular velocity in X, Y and Z axes in
Orientation sensor | virtual sensor that uses gravity and geomagnetic field to provide the orientation of the device in X, Y and Z axes
Sensor | Details
Accelerometer | 
Magnetometer | 
Gyroscope | 
Orientation sensor | virtual sensor that uses gravity and geomagnetic field to provide the orientation of the device in X, Y and Z axes
Orientation Angles [2]

## Slide 8: Application Specifications
Smartphone Specifications
Hardware Specifications
  Orientation sensor (virtual sensor)
  Tri-axial sensors
Feature | Specification
Model | Google Pixel 4a
Operating System | Android
Android Version | 12
Sensor | Specification
Accelerometer | LSM6DSR
Magnetometer | LIS2MDL
Gyroscope | LSM6DSR

## Slide 9: Data Collection and Analysis
Developed an android application
Developed a function to store the data in a comma separated value format
Developed python code for plotting and evaluation

## Slide 10: Raw Measurements
Data collection Specifications
Position
  Trouser pocket
  Shirt pocket
  In hand
Distance | 100m
Sampling rate | 50Hz
Mean acceleration of one step | 1.6S
Position of the Smartphone

## Slide 11: Raw Measurements
Location: Auepark near Auestadion, Angle – 290 degrees

## Slide 12: Raw Measurements
Orientation | Details
O1 | facing the screen towards the user
O2 | facing the screen towards the user and standing upside down
O3 | facing the screen away from the user
O4 | facing the screen away from the user and standing upside down
Smartphone Orientations

## Slide 13: Orientation Sensor
Using virtual orientation sensor

## Slide 14: Smartphone Orientation and Movement Direction Alignment (SOMDA)
Determine the top of the smartphone
Determine the screen of the smartphone and movement direction of the user
Flowchart of SOMDA [2]

## Slide 15: SOMDA - Trouser pocket
Determine the top of the Smartphone
  By using pitch angle
  Trouser pocket
    Pitch ≥ - smartphone upside down
    Pitch < - smartphone facing up
  Referred to as Roll Correction
  Always assumes to be perpendicular to the ground
  - Azimuth angle at time t
  - Roll angle at time t
  - Pitch angle at time t
  - Azimuth angle after roll correction

## Slide 16: SOMDA - Trouser pocket
Determine the screen of the smartphone and movement direction of the user
  By using peaks in the acceleration of the device along Z axis
  Windowed peak detection of window size ws= 1.6sec
  Threshold =

## Slide 17: SOMDA - Trouser pocket
Determine the screen of the smartphone and movement direction of the user
  SOMDA aligns the user orientation with smartphone by adding 180 degrees to azimuth angle
Information | Orientation
If the pitch angle is negative and negative peak is detected, then smartphone is facing towards the user | O1
If the pitch angle is positive and negative peak is detected, then smartphone is facing towards the user | O2
If the pitch angle is negative and positive peak is detected, then smartphone is facing away from the user | O3
If the pitch angle is positive and positive peak is detected, then smartphone is facing away the user | O4
- Compass Azimuth after smartphone orientation

## Slide 18: Implementing SOMDA on Orientation sensor

## Slide 19: SOMDA – Shirt pocket and Hand
Shirt Pocket and Hand
  Pitch angle gives negative angle as opposed to the trouser pocket position
Trouser Pocket | Shirt Pocket and Hand
Pitch < - smartphone facing up Pitch ≥ - smartphone upside down | Pitch > - smartphone facing up Pitch ≤ - smartphone upside down
Trouser Pocket | Shirt Pocket and Hand

## Slide 20: Evaluations – Orientation sensor
 | Mean Azimuth angle in degrees |  |  |  |  | 
Orientation | Trouser Pocket |  | Shirt Pocket |  | Hand | 
 | Before SOMDA | After SOMDA | Before SOMDA | After SOMDA | Before SOMDA | After SOMDA
O1 | 345 | 334 | 274 | 266 | 301 | 301
O2 | 160 | 331 | 106 | 285 | 124 | 304
O3 | 160 | 349 | 101 | 282 | 132 | 314
O4 | 339 | 347 | 281 | 282 | 298 | 297
Max Misalignment | 185 | 18 | 180 | 19 | 177 | 17

## Slide 21: Evaluations – Orientation Sensor
Accuracy evaluation – Ground Truth 290 degrees
  No orientation aligned with reference for trouser pocket at tolerance
Orientation | Accuracy Score at different tolerances with ground truth angle 290 degrees |  |  |  |  |  |  | 
 | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0 | 0 | 0 | 0.2 | 0 | 0.4 | 0.93 | 1
O2 | 0.55 | 0.93 | 1 | 1 | 0 | 0 | 0.67 | 1
O3 | 0.25 | 0.68 | 0.97 | 1 | 0 | 0 | 0 | 0.13
O4 | 0.17 | 0.72 | 0.99 | 1 | 0.2 | 0.8 | 0.98 | 1
Overall Accuracy (%) | 24.2 | 58.2 | 74 | 80 | 5 | 30 | 64.5 | 78.2
Orientation | Accuracy Score at different tolerances with ground truth angle 290 degrees |  |  |  |  |  |  | 
 | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0 | 0 | 0 | 0.2 | 0 | 0.4 | 0.93 | 1
O2 | 0.55 | 0.93 | 1 | 1 | 0 | 0 | 0.67 | 1
O3 | 0.25 | 0.68 | 0.97 | 1 | 0 | 0 | 0 | 0.13
O4 | 0.17 | 0.72 | 0.99 | 1 | 0.2 | 0.8 | 0.98 | 1
Overall Accuracy (%) | 24.2 | 58.2 | 74 | 80 | 5 | 30 | 64.5 | 78.2

## Slide 22: Evaluations – Orientation Sensor
Accuracy with reference orientation O2
100% in Hand, 84.3% in Shirt Pocket and 66.3% in trouser pocket at tolerance
Problem - deprecated
Orientation | Accuracy Score at different tolerances with ref orientation O2 |  |  |  |  |  |  |  |  |  |  | 
 | Trouser Pocket |  |  |  | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0.26 | 0.52 | 0.72 | 0.85 | 0 | 0.04 | 0.21 | 0.53 | 0.62 | 0.98 | 1 | 1
O3 | 0.18 | 0.29 | 0.41 | 0.49 | 0.47 | 0.81 | 0.98 | 1 | 0.12 | 0.47 | 0.92 | 1
O4 | 0.12 | 0.25 | 0.43 | 0.65 | 0.53 | 0.92 | 1 | 1 | 0.34 | 0.87 | 0.99 | 1
Orientation | Accuracy Score at different tolerances with ref orientation O2 |  |  |  |  |  |  |  |  |  |  | 
 | Trouser Pocket |  |  |  | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0.26 | 0.52 | 0.72 | 0.85 | 0 | 0.04 | 0.21 | 0.53 | 0.62 | 0.98 | 1 | 1
O3 | 0.18 | 0.29 | 0.41 | 0.49 | 0.47 | 0.81 | 0.98 | 1 | 0.12 | 0.47 | 0.92 | 1
O4 | 0.12 | 0.25 | 0.43 | 0.65 | 0.53 | 0.92 | 1 | 1 | 0.34 | 0.87 | 0.99 | 1

## Slide 23: Accelerometer and Magnetometer Orientation
Using Accelerometer and Magnetometer sensors
With rotation matrix in conjunction with orientation method
Parameter | Orientation sensor | Orientation Method
Angle | Measured in degrees | Measured in radians
Azimuth | Ranges between 0 and 360 degrees North :0, South :180, East :90, West :270 | Ranges between -π to +π North :0, South :π, East :π/2, West :-π/2
Pitch | Ranges between -180 to 180 | Ranges between –π/2 to π/2
Roll | Ranges between -90 to 90 | Ranges between -π to π

## Slide 24: Orientation Method
A lot of noise from compass
True direction is not possible
Requires filtering
Raw Measurements

## Slide 25: Fused Orientation
Gyroscope minimizes errors from accelerometer and Magnetometer
Induces drift over time
Using sensor fusion with gyroscope and orientation method
Complementary filter
  High pass filtering the drift accumulated in gyroscope
  Low pass filtering the accelerometer and magnetometer noise

## Slide 26: Fused Orientation
Raw Measurements

## Slide 27: Implementing SOMDA on Fused Orientation

## Slide 28: Evaluations – Fused Orientation
Accuracy evaluation
Orientation | Accuracy Score at different tolerances with ground truth angle at -70 degrees |  |  |  |  |  |  |  |  |  |  | 
 | Trouser Pocket |  |  |  | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0 | 0 | 0.01 | 0.21 | 0 | 0 | 0.07 | 0.77 | 0 | 0.44 | 1 | 1
O2 | 0.02 | 0.09 | 0.35 | 0.75 | 0 | 0.29 | 0.99 | 1 | 0 | 0 | 0.05 | 1
O3 | 0 | 0.02 | 0.34 | 0.72 | 0 | 0.48 | 0.99 | 1 | 0 | 0 | 0.02 | 0.67
O4 | 0 | 0.01 | 0.13 | 0.45 | 0 | 0.06 | 0.99 | 1 | 0 | 0.4 | 1 | 1
Overall Accuracy in (%) | 0.5 | 3 | 20.7 | 53.2 | 0 | 20.7 | 76 | 94.2 | 0 | 21 | 51.7 | 91.7
Orientation | Accuracy Score at different tolerances with ground truth angle at -70 degrees |  |  |  |  |  |  |  |  |  |  | 
 | Trouser Pocket |  |  |  | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0 | 0 | 0.01 | 0.21 | 0 | 0 | 0.07 | 0.77 | 0 | 0.44 | 1 | 1
O2 | 0.02 | 0.09 | 0.35 | 0.75 | 0 | 0.29 | 0.99 | 1 | 0 | 0 | 0.05 | 1
O3 | 0 | 0.02 | 0.34 | 0.72 | 0 | 0.48 | 0.99 | 1 | 0 | 0 | 0.02 | 0.67
O4 | 0 | 0.01 | 0.13 | 0.45 | 0 | 0.06 | 0.99 | 1 | 0 | 0.4 | 1 | 1
Overall Accuracy in (%) | 0.5 | 3 | 20.7 | 53.2 | 0 | 20.7 | 76 | 94.2 | 0 | 21 | 51.7 | 91.7

## Slide 29: Evaluations – Fused Orientation
Accuracy with reference orientation O2
100% in Hand, 100% in Shirt Pocket and 96.6% in trouser pocket at tolerance
Orientation | Accuracy Score at different tolerances with ref orientation O2 |  |  |  |  |  |  |  |  |  |  | 
 | Trouser Pocket |  |  |  | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0.33 | 0.62 | 0.8 | 0.92 | 0.17 | 0.86 | 1 | 1 | 0.38 | 0.90 | 1 | 1
O3 | 0.54 | 0.85 | 0.97 | 0.99 | 0.87 | 1 | 1 | 1 | 0.97 | 1 | 1 | 1
O4 | 0.54 | 0.77 | 0.92 | 0.99 | 0.96 | 1 | 1 | 1 | 0.41 | 1 | 1 | 1
Orientation | Accuracy Score at different tolerances with ref orientation O2 |  |  |  |  |  |  |  |  |  |  | 
 | Trouser Pocket |  |  |  | Shirt Pocket |  |  |  | Hand |  |  | 
O1 | 0.33 | 0.62 | 0.8 | 0.92 | 0.17 | 0.86 | 1 | 1 | 0.38 | 0.90 | 1 | 1
O3 | 0.54 | 0.85 | 0.97 | 0.99 | 0.87 | 1 | 1 | 1 | 0.97 | 1 | 1 | 1
O4 | 0.54 | 0.77 | 0.92 | 0.99 | 0.96 | 1 | 1 | 1 | 0.41 | 1 | 1 | 1

## Slide 30: Comparison of Orientation Sensor and Fused Orientation approach
Comparing overall accuracy in percentage with reference orientation O2 for the two approaches
Position | Orientation Sensor |  |  |  | Fused Orientation |  |  | 
Trouser Pocket | 19 | 35.3 | 51.6 | 66.3 | 47 | 74.6 | 89.6 | 96.6
Shirt Pocket | 32.6 | 57.6 | 72.6 | 84.3 | 66.6 | 95.3 | 100 | 100
Hand | 36 | 77.3 | 97 | 100 | 58.6 | 96.6 | 100 | 100
Position | Orientation Sensor |  |  |  | Fused Orientation |  |  | 
Trouser Pocket | 19 | 35.3 | 51.6 | 66.3 | 47 | 74.6 | 89.6 | 96.6
Shirt Pocket | 32.6 | 57.6 | 72.6 | 84.3 | 66.6 | 95.3 | 100 | 100
Hand | 36 | 77.3 | 97 | 100 | 58.6 | 96.6 | 100 | 100

## Slide 31: Conclusions & Future Work
Implemented existing orientation approach.
SOMDA implementation
Implemented new orientation approach
Comparison of the two approaches
  Fused Orientation approach performing better for all the three positions
  Smartphone position in hand is better, then comes the shirt pocket and least in the trouser pocket
Future work:
  A way to classify the position of the smartphone
  Machine Learning

## Slide 32: References
[1] bankmycell.com. “HOW MANY SMARTPHONES ARE IN THE WORLD”. 2022. url: https://www.bankmycell.com/blog/how-many-phones-are-inthe-world (visited on 04/01/2022).
[2] Rico Kusber et al. “Direction Detection of Users Independent of Smartphone Orientations”. In: 2015 IEEE 82nd Vehicular Technology Conference (VTC2015- Fall). 2015, pp. 1–6. doi: 10.1109/VTCFall.2015.7390890.
[3] Takumi Matsumoto and Masahiro Fujii. “A study on estimation of traveling direction for pedestrian dead reckoning by using inertial sensors”. In: 2020 27 IEEE 9th Global Conference on Consumer Electronics (GCCE). 2020, pp. 465– 466. doi: 10.1109/GCCE50665.2020.9291953.